## Slide 1
Deep Reinforcement Learning Project
Spring 2026
Process-Focused Report
Autonomous Parallel Parking Using Soft Actor-Critic (SAC) Algorithm
An Iterative Approach to Reward Engineering & Problem Solving
Presenters
Cem Irer & Idil Balandı

## Slide 2
The Urban Parking Challenge
Autonomous parallel parking requires precise control in constrained urban environments. The vehicle must maneuver into a tight slot with minimal error, requiring multi-phase planning:
Approach phase with velocity control
Orientation alignment (Heading control)
Final positioning (Lateral control)
Why Reinforcement Learning?
Handling Complexity
Learns complex non-linear dynamics difficult to model with PID
Generalization
Adapts to varied starting positions better than rule-based systems
Vehicle Specs
VW ID.4 Model
Length
4.77 m
Width
2.04 m
Wheelbase
3.00 m
Steering Limit
±35°
Environment Specs
Constraints
Parking Slot Length
6.00 m Tight
Parking Slot Width
2.50 m Tight
Longitudinal Margin
1.23 m (Total)
Lateral Margin
0.46 m (Total)
Problem Definition
Real-World Challenge & Vehicle Specifications

## Slide 3
13D State Space (s)
s = [ x, y, θ, v, # Ego State (4D)
Δx, Δy, Δθ, # Target Relative (3D)
xmin, xmax, ymin, ymax, # Boundaries (4D)
dobs1, dobs2 ] # Obstacles (2D)
All inputs are normalized to [-1, 1] for neural network stability.
2D Action Space (a)
a = [ δ, acc ]
Steering (δ)
[-1, +1] → [-35°, +35°]
Acceleration (acc)
[-1, +1] → [-0.5, +0.5] m/s²
Bicycle Kinematic Model
X-Velocity
ẋ = v cos(θ)
Y-Velocity
ẏ = v sin(θ)
Angular Vel
θ̇ = (v / L) tan(δ)
Acceleration
v̇ = a
Wheelbase (L): 3.0m
dt: 0.05s (50Hz)
Termination Conditions
Success
4 vehicle corners inside parking slot boundaries
Collision
Vehicle body intersects with obstacle or boundary
Timeout
Episode length > 500 steps (25 seconds)
Autonomous Parallel Parking Project
Mathematical Formulation • Slide 3
Mathematical Formulation
Markov Decision Process (MDP)

## Slide 4
Why Soft Actor-Critic (SAC)?
Core Advantages for Parking Task
Off-Policy Efficiency
Reuses past experiences from a replay buffer, crucial for sample-efficient learning within limited compute budget.
Maximum Entropy
Encourages exploration by maximizing entropy alongside reward. Prevents premature convergence to local optima.
Continuous Control
Directly outputs smooth steering/acceleration values without discretization artifacts, essential for precise maneuvering.
Stability
Uses twin Q-networks (clipped double Q-learning) to reduce value overestimation bias.
Architecture
Action a
a
a
State s
Actor π
Critic Q1
Critic Q2
Env
Q Value 1
Q Value 2
4

## Slide 5
Hyperparameters & First Steps of Environment
Hyperparameters
Learning Rate | 3e-4 (Adam)
Replay Buffer | 100,000 transitions
Batch Size | 256
Network Structure | MLP [256, 256] (ReLU)
Discount (γ) | 0.99
Total Timesteps | 300,000
4
Obstacle 1
Obstacle 2
TARGET SLOT
6.0m x 2.5m
VW ID.4
Y
X
30.0m (Road Length)
Parking Zone
15.0m
Slot Size: 6.0m × 2.5mv
Margin: Tight (0.6m fwd/back)
Config: Parallel (Street-side)

## Slide 6
Gymnasium Architecture
Custom Environment: Built on Gymnasium interface inheriting from gym.Env
Observation Space: 13D continuous vector normalized to [-1, 1]
Ego state, Relative target, Boundaries, Obstacles
Action Space: 2D continuous control
Steering [-35°, +35°], Acceleration [-0.5, +0.5] m/s²
Reward System Design
Stage 0
Approach (>5.5m)
Stage 1
Y-Correction (3.0m - 5.5m)
Stage 2
Entry & Alignment (<3.0m)
Constraints & Safety
Safety Barriers: Exponential penalty near boundaries
Collision Check: Oriented bounding box intersection (SAT)
Speed Limits: Global max 1.0 m/s, parking zone max 0.5 m/s
Episode Settings
Time Step
dt = 0.05s (20Hz)
Max Length
500 steps (25s)
Initialization
Randomized spawn near parking zone
Position +/- 2m, Angle +/- 15°
Gymnasium Custom Env • Bicycle Kinematics • Staged Rewards
Slide 5
Environment Implementation

## Slide 7
Initial Approach: Complex Reward System
Iteration 1 (0 - 50k Steps)
FAILED ATTEMPT
Attempt 1
The Over-Engineered Reward Function
12+ components with separate weights attempting to control every aspect of motion
Problems Encountered
Over-Parameterized: 20+ hyperparameters made tuning impossible (curse of dimensionality)
Hard to Debug: Couldn't identify which component was causing bad behavior
Unpredictable Behavior: Components canceled each other out (e.g., smoothness vs. progress)
OUTCOME: Agent stuck at 5-6m distance
Failed to approach parking area. Policy collapsed to "do nothing" to avoid penalties.
06
Rtotal = r_progress + r_safety + r_smoothness + r_effort + r_time
+ r_anti_stagnation + r_anti_oscillation + r_y_direction
+ TERMINAL_REWARDS

## Slide 8
Iteration 2: Simplification & Progress
50k - 150k Steps
PARTIAL SUCCESS
What Worked
Simplified Reward Structure
Reduced 12+ components to 6 core terms to isolate behaviors:
R = -d - |Δθ| - y_dist
+ Δd + Δθ + terminal
Observable Improvements
Agent successfully learned to approach the parking area
Reliable distance reduction from start (25m → 2m)
Collision rate dropped significantly
New Discovery
The "False Attractor" Problem
Stalled Progress: Agent gets stuck at 1.8 - 2.0m distance
Deceptive Metrics: Perfect angle (~2°) but absolute failure to enter slot
Entry Failure: 0/4 corners inside parking slot
Key Insight
The agent found a local maximum: "Standing still with good angle is safer than trying to park."
07

## Slide 9
Root Cause Analysis
The "False Attractor" Problem (215k Steps)
Situation at 215k Steps
Agent State Breakdown
Current Position
(18.11, 6.70)
Target Position
(17.50, 8.50)
Y-Axis Error
1.60m (Critical!)
Heading Error
~2.0° (Excellent)
Speed
~0.05 m/s (Stuck)
TOP-DOWN VIEW RECONSTRUCTION
TARGET SLOT
AGENT
Agent aligns angle perfectly but fails to enter slot due to Y-axis gap
Identified Root Causes
Fixed Bonuses Exploitation
Reward `+30` given for ANY approach. Agent learned to make microscopic movements to farm rewards without risking entry.
No Standing Penalty
Lack of penalty for zero velocity allowed the agent to "park" outside the slot indefinitely once angle was minimized.
Weight Imbalance
Angle penalty (50.0) dwarfed Y-penalty (5.0). Agent optimized the easier objective (heading) and ignored the harder one (position).
Absolute State Reward
Rewarded `total_corners_inside` instead of `new_corners`. Standing with 0 corners was safer than risking collision to get 1.
Key Insight: The agent found a local maximum where Risk(Entry) > Reward(Status Quo). We needed to invert this equation.
Risk(Entry) > Reward(Status Quo)
08

## Slide 10
Stage 0: APPROACH
> 5.5m
Goal
Learn to move towards parking area without rushing
- 0.3 · d
Light distance penalty
+ 250 · Δd
Delta-Proportional Progress
- 2 (if stuck)
Minimal stall penalty
Safe Exploration: Reward floored at -50, weak safety barriers
Stage 1: Y-DIRECTION
5.5m - 3.0m
Goal
Align vertical position (Y-axis) with parking slot
- 0.5 · d
Moderate distance penalty
- 2.0 · |y - y_tgt|
Y-Distance Penalty
+ 300 · Δy_up
Bonus for moving UP
- 400 · |Δy_down|
Penalty for moving DOWN
Vertical Focus: Strong incentives to correct Y-offset before arrival
Stage 2: ENTRY
< 3.0m
Goal
Fix angle, enter slot, prevent false attractor
- 20.0 · |y - y_tgt|
- 50.0 · |Δθ|
Angle Penalty
+ 600 · Δcorners
NEW Corners Only
- 80 (if standing)
Anti-Stagnation
- 500 · retreat
No Retreat Allowed
Precision Mode: Full constraints, massive penalties for errors
Iteration 3: Staged Reward System Implementation
Slide 9
Solution: Staged Reward System
Matching Reward Complexity to Task Phase
SOLVED FALSE ATTRACTOR

## Slide 11
Deadlock Detection
Prevents agent from exploiting "safe spots" without making progress.
if |Δd| < 0.01 for 40 steps:
terminate = True
reward -= 300
Stuck
Detect
Terminate & Penalize
False Attractor Killer
Specifically targets the local minimum at 2m distance.
if speed < 0.05 and angle_err > 10°:
reward -= 80 (Standing)
reward -= 300 (Wrong Pose)
Curriculum Learning Strategy
Goal: Guide agent from simple tasks to complex maneuvers progressively.
Adaptive Difficulty • Anti-Stagnation Logic
Slide 10
1
Early Episodes (0-50k)
Spawn very close to parking slot (1-2m). Gentle constraints allow easy exploration of the target area.
2
Mid Training (50k-150k)
Spawn distance increases to medium range (3-5m). Introduction of stricter Y-axis penalties.
3
Final Stage (150k+)
Full hard difficulty spawn (6m+). Full constraints enabled. Simulates real-world parallel parking scenario.
Additional Fixes & Curriculum
Refining Learning Stability

## Slide 12
Code Structure & Organization
parking_rl/
envs/
parking_env.py
806 lines
# Core logic, Kinematics, Rewards
antagonist_wrapper.py
# Curriculum interface
agents/
antagonist.py
# Progressive difficulty agent
configs/
config.py
# Dataclasses, Hyperparameters
models/
# Saved checkpoints (.zip)
train.py
# Training loop, Logging
demo.py
# Visualization & Inference
evaluate.py
# Metric calculation
Modular Architecture
Separation of concerns between environment logic, agent implementation, and configuration management allows for easier debugging and extension.
Production Standards
Comprehensive Type Hints and Docstrings across all modules ensuring code readability and maintainability.
Config-Driven
All hyperparameters centralized in config.py using Dataclasses. No hardcoded magic numbers in logic files.
Modular Reward System
Reward components implemented as separate private methods for granular testing and weight tuning.
Production-Grade Python Implementation
Slide 11

## Slide 13
The development process revealed critical lessons in reward engineering and RL system design that go beyond simple parameter tuning.
1
Simplicity > Complexity
Our initial 12+ component reward function was impossible to debug. Reducing to core components per stage made behavior predictable and identifiable.
Design for debuggability
2
Reward Progress, Not State
Fixed bonuses for "being in a good state" led to exploitation. Using delta-proportional rewards (rewarding change) incentivized continuous improvement.
Always use deltas (Δ)
3
Explicitly Prevent Local Minima
The agent found a "false attractor" by standing still at a safe distance. We had to add explicit penalties for stagnation and lack of progress to force movement.
Anticipate false attractors
4
Priorities via Weights
The agent ignored Y-positioning because the penalty (5.0) was weak compared to angle (50.0). Boosting critical dimensions to 20.0 forced learning.
Weight reflects priority
5
Exploration Needs Safety
Early training failed when penalties were too harsh. Implementing reward floors and weaker constraints in early stages allowed necessary exploration.
Don't crush exploration
6
Design for Observability
We couldn't fix what we couldn't see. Adding detailed logging, stage tracking, and reward component breakdowns was crucial for the final breakthrough.
Log everything
Project Retrospective • Key Lessons
Slide 12
What We Learned - Key Insights

## Slide 14
What Worked Well
Staged Reward System: Breaking the task into Approach → Y-Align → Entry phases simplified learning.
Delta Bonuses: Rewarding improvement (Δ) instead of state prevented exploitation.
Deadlock Detection: Automatically terminating stuck episodes saved training time.
Curriculum: Progressive spawn difficulty helped early stabilization.
What Didn't Work
Over-Complex Rewards: Initial 12+ component function was undebuggable chaos.
Fixed Bonuses: Providing constant reward for "being close" created false attractors.
Weak Y-Penalty: Initial weight (5.0) was ignored in favor of angle optimization (50.0).
Current Constraints
Limited Compute
~300k Steps
Single Seed
Single Scenario
Due to time constraints, we couldn't perform extensive hyperparameter sweeps or multi-seed robustness testing.
If We Started Over...
"We would implement the staged reward system from Day 1 and prioritize logging detailed reward component breakdowns immediately. We spent 50% of our time fighting a complex reward function that was fundamentally flawed."
Honest Assessment • Project Constraints
Slide 13
Challenges & Limitations

## Slide 15
01
02
03
04
05
Novel Approaches & Implementation Quality
Slide 14
Three-Stage Reward Engineering
Designed a novel progressive system matching reward complexity to task phases (Approach → Position → Entry) with reward floors for safe exploration.
Delta-Proportional Shaping
Shifted from rewarding absolute states to rewarding improvement (Δ) across all objectives, completely eliminating static state exploitation.
False Attractor Prevention
Identified and solved local minima via explicit penalties for stagnation (standing still), retreat, and deadlock detection mechanisms.
Integrated Curriculum Strategy
Implemented an adaptive spawning system that increases task difficulty (distance and angle constraints) linearly with training progress, stabilizing early learning.
Production-Grade Codebase
Delivered a robust 806-line custom Environment with comprehensive type hinting, modular reward components, and configuration management for reproducibility.
Technical Contributions
Key Innovations & Engineering

## Slide 16
Qualitative Progress Indicators
Collision Rate
High Low
Target Approach
Random Consistent
Angle Control
Erratic Precise (~2°)
Y-Positioning
Ignored Learning...
Training Progression Timeline
Slide 15
Phase 1: Exploration
0 - 50k Steps
Random actions
High collision rate
No directional sense
Phase 2: Approach
50k - 150k Steps
Consistent pathing
Safety improved
Stalls at ~5m dist
Phase 3: Stagnation
150k - 215k Steps
Good angle (~2°)
False attractor found
Y-axis ignored
Phase 4: Correction
215k - 300k Steps
Staged rewards active
Y-correction focus
Training ongoing...
1
2
3
Experimental Results - Process Focus

## Slide 17
With the core staged reward system validated, future work will focus on robustness, generalization, and transferability to physical systems.
Hyperparameter Optimization
Systematic grid search over Y-penalty weights [10-30] and stage transition thresholds to find the optimal trade-off between position accuracy and training speed.
Curriculum Extensions
Expanding the curriculum to include variable parking slot sizes (5.5m - 7.0m) and varied spawn orientations to improve policy generalization.
Algorithm Comparisons
Benchmarking SAC against PPO (on-policy stability) and TD3 (deterministic control) to empirically validate the choice of algorithm for parking tasks.
Sim-to-Real Preparation
Introducing domain randomization, sensor noise (Gaussian ±0.1m), and actuator delays to bridge the gap between idealized simulation and physical hardware.
Multi-Task Learning
Training a single unified policy capable of handling angle parking, perpendicular parking, and garage scenarios using context-aware observation spaces.
Next Step
Deploying current policy to
Hardware-in-Loop (HIL) testbench
Research Extensions • 2024-2025
Slide 17
Future Roadmap
Planned Extensions & Research Directions

## Slide 18
Conclusion
Final Project Submission
Slide 18
Implemented production-grade Autonomous Parallel Parking with SAC in custom Gym environment
Designed novel Staged Reward System to solve complex multi-phase maneuver task
Identified and fixed critical "False Attractor" local minimum using root cause analysis
Demonstrated systematic, iterative engineering approach over simple parameter tuning
Core Learning Outcomes:
Reward Engineering is Critical
Simplicity Facilitates Debugging
Prevent Local Minima
Staged Approaches Match Intuition
"RL reward engineering is iterative. We failed, learned, and redesigned. The journey of debugging and fixing IS the learning process."